| PHYSICAL SPECIFICATION |
| --- |
| Nominal Voltage Nominal Capacity (10HR) | 12V 42Ah |  |
| Dimension | Length Width Container Height Total Height | 198±2mm （7.80 inches） 166±2mm (6.53 inches) 170±2mm (6.69 inches) 170±2mm (6.69 inches) |  |
| Weight | Approx. 14.8Kg ( 32.6lbs) |  |
| Standard Terminal | Bolt-and-nut lead terminal Bolt Type: M6 |  |
| ELECTRICAL SPECIFICATION |
| Characteristics | Discharge curves @ 25℃ (77 °F) |
| Capacity | 10 hour rate (4.2A) 5 hour rate (7.14A) 3 hour rate (10.5A) 1hour rate (25.2A) | 42Ah 35.7Ah 31.5Ah 25.2Ah |  |
| Capacity affected by temperature | 40℃ （104 0F） 25℃ （77 0F） 0℃ （32 0F） | 102% 100% 85% |  |
| Self Discharge | 3% of capacity declined per month at (25℃) |  |
| Internal Resistance | Full charged battery (25℃,77 0F) 9.8mΩ |  |
| Constant Voltage Charge | Cycle | Initial Charging Current less than 10.5A Voltage 14.1~14.4V at 25℃ (77 0F ) Temperature Coefficient –5mV/℃ |  |
|  | Standby | No limit on Initial Charging Current Voltage 13.5~13.8V at 25℃ (77 0F ) Temperature Coefficient –3.3mV/℃ |  |